## Slide 1: FRC 1159 Software team tasks

## Slide 2: Tasks
Lear LabVIEW
Lear how to program the Robot
Program the Radio
Imaging the RoboRIO
Make a build
Deploy a build
Lear how to program the motor controllers
Learn how to use Github

## Slide 3: Learn Labview

## Slide 4: Install Labview and tools
Install LabVIEW for FRC
Install the FRC Game Tools

## Slide 5: Install Labview and tools
Installation Instructions for Teams Using LabVIEW for Development
This option allows you to program your robot in LabVIEW, perform vision analysis, and capture from USB cameras.
Launch the installer. This will initiate a pre-install of NI Package Manager. After the NI package manager installation completes, you will be presented with a list of software to install.
On the "Select Products" dialog, accept the default selections. This includes:
  LabVIEW (32-bit) English - 2020 SP1
  LabVIEW Real-Time Module English - 2020
  Vision Development Module - 2021

## Slide 6: Install Labview and tools
  LabVIEW Robotics Module for FRC - 2020
  NI CompactRIO - 21.0.0
  NI-IMAQdx driver - 21.0.0
On the "Additional items you may wish to install" dialog, accept the default selections. NOTE: If you do not accept the default selections, it is likely that some components required for programming your robot will not be installed.
Accept the licensing agreements and proceed through the installation wizard.
This option has the following system requirements:
  Operating System: Windows 10/8.1
  Free Space Before Install: 42.1GB Free Space After Vision Install: 35.1GB Free Space after full install: 19.6 Disk Footprint: 15.2 GB

## Slide 7: Install Labview and tools
To Activate LabVIEW
Login to National Instruments
Username: ramonarampage@gmail.com
Password: ramona1159
Enter the serial number to activate:
B05P07428

## Slide 8: Install Labview and tools
Once LabVIEW and the FRC Game Tools are installed, when LabVIEW starts up it should look like this 

## Slide 9: LABVIEW tutorials
You can access all the tutorials listed here from the Tutorials tab.
The tutorials are quick and to the point.

## Slide 10: LABVIEW tutorials
Learn NI LabVIEW Basics
Getting Started with LabVIEW
FRC LabVIEW Tutorial
Fundamentals of LabVIEW for FRC - Episode 1
Fundamentals of LabVIEW for FRC: Episode 2 - Vision and Control
Fundamentals of LabVIEW for FRC: Episode 3 - Command and Control Architecture
Fundamentals of LabVIEW for FRC: Episode 4 - Source Code Control and Tips & Tricks

## Slide 11: Useful links
Most of the links on this presentation come from the link below
Control System and Programming Documentation

## Slide 12: Learn to Program the robot

## Slide 13: Hardware & software overview
Hardware Component Overview
Software Component Overview

## Slide 14: Frc labview programming
Installing LabVIEW for FRC (LabVIEW only)
Installing the FRC Game Tools
Re-licensing LabVIEW for 2021 Season
Creating Robot Programs
  Creating, Building and Loading your Benchtop Test Program
  Tank Drive Tutorial
  Command and Control Tutorial
LabVIEW Resources
  LabVIEW Resources
  Waiting for Target to Respond - Recovering from bad loops

## Slide 15: Frc labview programming
  Talon SRX CAN
  How To Toggle Between Two Camera Modes
  LabVIEW Examples and Tutorials
  Add an Independent Motor to a Project
  Keyboard Navigation with the roboRIO
  Making a One-Shot Button Press
  Adding Safety Features to Your Robot Code
  How to Use Joystick Buttons to Control Motors or Solenoids
  Local and Global Variables in LabVIEW for FRC
  Using the Compressor in LabVIEW

## Slide 16: FRC WPI Robotics Library Overview
  FRC WPI Robotics Library Overview
  The link above takes to the topics below
  Introduction
  RobotDrive
  Sensors
  Actuators
  I/O
  Driver Station
  Camera
  Communication
  Utilities
  Power

## Slide 17: Programming motor control

## Slide 18: Programming motor control
Motor
Motor Controller
PDP – Power Distribution Panel

## Slide 19: Programming motor control
Basic Motor Control Tutorial
  Click on the link above to learn how to make the motor control program below

## Slide 20: Programming motor control

## Slide 21: Drive motors
Initialize
Control
Close

## Slide 22: Drive motors – Initialize motors
The following code goes in Begin.vi

## Slide 23: Drive motors – control Motors
The following code goes in Teleop.vi

## Slide 24: Drive motors – close motors
The following code goes in Finish.vi

## Slide 25: Other motors
Add an Independent Motor to a Project
Initialize
Use
Close

## Slide 26: Other motors - initialize
FIRST, create a motor reference in the Begin.vi, using the Motor Control Open VI and Motor Control Refnum Registry Set VI. These can be found by right-clicking in the block diagram and going to WPI Robotics Library>>RobotDrive>>Motor Control. Choose your PWM line and name your motor. I named mine “Lift Motor” and connected it to PWM 7. (I also included and enabled the Motor Control Safety Config VI, which automatically turns off the motor if it loses connection.)

## Slide 27: Other motors – Use it
Now, reference your motor (the name has to be exact) in the Teleop.vi using the Motor Control Refnum Registry Get VI and tell it what to do with the Motor Control Set Output VI. These are in the same place as the above VIs.

## Slide 28: Other motors – example
For example, the next snippet tells the Lift Motor to move forward if button 4 is pressed on Joystick 0 and to remain motionless otherwise. For me, button 4 is the left bumper on my Xbox style controller (“Joystick 0”). For much more in-depth joystick button options, check out How to Use Joystick Buttons to Control Motors or Solenoids.

## Slide 29: Other motors – close
Finally, we need to close the references in the Finish.vi (just like we do with the drive and joystick), using the Motor Control Refnum Registry Get VI and Motor Control Close VI. While this picture shows the Close VI in a flat sequence structure by itself, we really want all of the Close VIs in the same frame. You can just put these two VIs below the other Get VIs and Close VIs (for the joystick and drive).

## Slide 30: Joysticks
Initialize
Close
Assign controls
Retrieve values

## Slide 31: Joysticks - initialize
The following code goes in Begin.vi

## Slide 32: Joysticks – Assign buttons

## Slide 33: Joysticks – Driver station

## Slide 34: Joysticks – Assign buttons

## Slide 35: Joysticks – Assign buttons

## Slide 36: Joysticks – Read joystick values
The following code goes in Teleop.vi

## Slide 37: Joysticks

## Slide 38: Joysticks – close joystick
The following code goes in Finish.vi

## Slide 39: Camera
Program

## Slide 40: sensors
Program

## Slide 41: Setting up the robot radio
Note At official FRC events, you must use the FRC Radio Kiosk at the inspection table to configure your radio.

## Slide 42: Setting up the robot radio
Programming your Radio
What is the Radio?
Download Radio programming tool (installer)
Diagram
Program Radio

## Slide 43: Download the robot radio tool
Download Radio programming tool (installer)
FRC Radio Configuration 20.0.0

## Slide 44: robot radio description

## Slide 45: Wiring the robot radio

## Slide 46: Setting up the robot radio
 | Note If the roboRIO Imaging Tool fails to update the roboRIO, turn off Windows Firewall in the Control Panel of Windows.
Configuring the Radio for Competitions
Complete the following steps to configure a radio for development.
Launch the Radio Configuration Utility that you installed from this link
In the Network Interfaces dialog of the utility, select the network interface (the Ethernet port) your radio is connected to and press OK.

## Slide 47: Setting up the robot radio
 | Note If the roboRIO Imaging Tool fails to update the roboRIO, turn off Windows Firewall in the Control Panel of Windows.
In the utility, enter your team number, choose your radio type, and follow the directions
When you press Configure, you should see a Configuration Progress dialog followed by a Complete dialog.

## Slide 48: Imaging the roborio

## Slide 50: Imaging the roborio
Imaging your roboRIO
Instructions
Check RoboRIO firmware

## Slide 51: Imaging the roborio
 | Note If the roboRIO Imaging Tool fails to update the roboRIO, turn off Windows Firewall in the Control Panel of Windows.
Setting up the roboRIO
You must configure the roboRIO and the Axis camera (if using one) before you can run a robotics program on the robot.
To configure the roboRIO, you must A) connect the computer to the roboRIO, and then B) run the roboRIO Imaging Tool.
A) Connecting the Computer to the roboRIO
Use a USB cable to connect the computer (USB A-Type) to the USB Device Port (USB B-Type) of the roboRIO (the single USB port next to the INPUT power). Then configure the roboRIO with the roboRIO Imaging Tool.
B) Running the roboRIO Imaging Tool
Considerations Before Running the roboRIO Imaging Tool
Do not use the roboRIO Imaging Tool on the roboRIO over a wireless connection. If the connection is lost, the data that the roboRIO Imaging Tool writes to the roboRIO is corrupted.
Do not use the roboRIO Imaging Tool on the roboRIO over Ethernet. While this should work, it is not as reliable as USB.
Do not use Measurement & Automation Explorer (MAX) to install additional software on the roboRIO. MAX overwrites the FRC VIs on the roboRIO. If you use MAX to install additional software on the roboRIO, you must use the roboRIO Imaging Tool to restore the device to a usable state.

## Slide 52: Imaging the roborio
 | Note If the roboRIO Imaging Tool fails to update the roboRIO, turn off Windows Firewall in the Control Panel of Windows.
Running the roboRIO Imaging Tool
Complete the following steps to configure the roboRIO with the roboRIO Imaging Tool.
Select roboRIO Imaging Tool 2020 from the Utilities tab of the LabVIEW Getting Started Window, or by selecting Tools»roboRIO Imaging Tool... from within LabVIEW, or by double-clicking the roboRIO Imaging Tool shortcut on the Windows Desktop.
Select the roboRIO you want to configure from the roboRIO Targets table. This table lists all roboRIOs connected to the host computer.
Choose the task for the imaging tool to perform:
  Edit Startup Settings allows you to change startup settings and your team number.
  Format Target is used to image the roboRIO and set your team number. From the Select Image list, select the most recent .zip file to download the most recent image to the roboRIO. If you do not see a .zip file, you must install the FRC Game Tools. Enter your team number in the Team Number text box, and click the Reformat button to download the image to the roboRIO. Do not turn off power to the roboRIO or interfere with the USB connection while the roboRIO Imaging Tool downloads the image to the roboRIO.
  Update Firmware is used to download the latest firmware to the roboRIO. The minimum required firmware for FRC 2020 is version 5.0.0. The latest firmware version is 6.0.0, and is included with this update. To update, choose the latest .cfg file from the Select Firmware list and click the Update button. Do not turn off power to the roboRIO or interfere with the USB connection while the roboRIO Imaging Tool updates the roboRIO firmware.

## Slide 56: Program the motor controllers

## Slide 57: template
template

## Slide 58: Make a robot program build

## Slide 59: template
template

## Slide 60: template
template

## Slide 61: template
template

## Slide 62: template
template

## Slide 63: template
template

## Slide 64: template
template

## Slide 65: template
template

## Slide 66: Deploy the robot program build

## Slide 67: template
template

## Slide 68: Learn to use github

## Slide 69: Github
Get a Github account
Learn to how use it
Link to team’s Github
Checkout code
Check in code

## Slide 70: Template section divider

## Slide 71: Team’s progress

## Slide 72: Software team’s progress

## Slide 73: resources
http://www.ni.com/first
https://www.firstinspires.org/resource-library/frc
http://www.chiefdelphi.com
Technical>Programming>LabVIEW

## Slide 74: LABVIEW tutorials
Getting Started with LabVIEW
FRC LabVIEW Tutorial
Fundamentals of LabVIEW for FRC - Episode 1
Fundamentals of LabVIEW for FRC: Episode 2 - Vision and Control
Fundamentals of LabVIEW for FRC: Episode 3 - Command and Control Architecture